## Slide 1: Low Cost Crowd Counting using Audio Tones
Pravein Govindan Kannan1, Seshadri Padmanabha Venkatagiri1, Mun Choon Chan1, Akhihebbal L. Ananda1 and Li-Shiuan Peh2
1School of Computing,
National University of Singapore
2Computer Science and Artificial Intelligence Laboratory,
Massachusetts Institute of Technology
Notes: OM NAMO GANAPATHAYEN NAMAHA

## Slide 2: Outline
Why Crowd Counting?
Why Audio Tones?
Our System
Some Measurements
Evaluation

## Slide 3: Why Crowd Counting?
Event Planning4
Proximity Marketing5

## Slide 4: Why Crowd Counting?
Public Transport Shelters6
Public/Private Commutation Services7

## Slide 5: Crowd Counting Using Audio Tones
Ubiquity of smart phones1
Microphone/Speaker as communication devices2,3
Audio tones for communication
Crowd Counting

## Slide 6: Outline
Why Crowd Counting?
Why Audio Tones?
Our System
Some Measurements
Evaluation

## Slide 7: Why Audio Tones?
No Special Hardware: Speakers and Microphones are available in almost all mobile devices.
Power: Consumes less power than existing technologies such WiFi and 3G
Scalable: Can propagate multi-hop. Difficult to achieve with RFID
Anonymous: Unlike 3G, WiFi and Bluetooth, this does not disclose the smartphone’s identity

## Slide 8: Outline
Why Crowd Counting?
Why Audio Tones?
Our System
Some Measurements
Evaluation

## Slide 9: Our proposal based on Audio Tones…
Requires NO infrastructure
Reports upto 90% accurate count
Consumes at least 80% less power than WiFi and 3G
Can count upto 900 devices

## Slide 10: System

## Slide 11: Uniform Hashing
Frequency
Set
F1
F2
F3
F4
F5
F6
S
F1
F2
F1
F2
F3
F2
F3
F4
F3
F4
F1
F2
F3
F1
F2
F3
F4
F1
F2
F3
F4
F2
F3
F4
F1
F2
F3
F4
F1
F2
F3
F4
F1
F2
F3
F4
F1
F2
F3
F4
Round 1
Round 2
Round 3
Notes: Notice that in each round each node can send out unique frequency. Multihop frequency transmission ensures redundancy

## Slide 12: Uniform Hashing
If frequency Fi is received by a phone, bit (i – 1) in the bitmap is 1, and 0 otherwise. For the previous example, bitmap is:
1
1
1
Bit 0, LSB
Bit 1
Bit 2
1
Bit 3
Estimated Count = Number of ones in the bitmap

## Slide 13: Uniform Hashing
Number of nodes that can be counted scales linearly with frequencies available
Over-counts in the presence of ambient noise
Under-counts if two or more nodes pick the same frequency

## Slide 14: Geometric Hashing
Frequency Set
F1
F2
F3
F4
F5
F6
S
PERFORM MULTIPLE ROUNDS SIMILAR TO UNIFORM HASHING
NOTE: Only 3 frequencies are used for 6 nodes
Notes: ½ phones are likely to map to F_1, ¼ to second and 1/8 to the third. Therefore, we need only 3 frequencies to represent 6 phones

## Slide 15: Geometric Hashing
R = 2
But, E[R] has high variance, We use multiple simultaneous counting processes to improve accuracy
For the previous example, bitmap is:
1
1
0
Bit 0, LSB
Bit 1
Bit 2
Find the rightmost zero, R.
Estimated Count is 1.2897 * 2E(R) [From FLAJOLET et al. JCSS’1985. Used for duplicate-insensitive counting database records], where E(R) is expected value of R
Estimated Count = 5.156
Notes: Its unbiased estimate. It has very high bit rate. Using single estimate could have high variance. To address this, we should have many estimates.

## Slide 16: Geometric Hashing
Frequency Set
F1
F2
F3
F4
F5
F6
S
Counting Process 1, R1 = 2
Counting Process 2, R2 = 3
E[R] = (R1 + R2)/2 = 2.5, Estimated Count = 7.3
Notes: We divide the freq set into multiple subsets in order to perform multiple estimation in parallel. Note that it is possible with GH since n freq can support upto 2^n devices

## Slide 17: Geometric Hashing
Duplicate Insensitive
Scales logarithmically with frequencies. n frequencies can count 2n
Utilizes multiple simultaneous estimations to increase accuracy

## Slide 18: Outline
Why Crowd Counting?
Why Audio Tones?
Our System
Some Measurements
Evaluation

## Slide 19: Measurement and Evaluation: Tools
Hardware | 20 Google Nexus S, 5 Galaxy Nexus 1 HTC Desire, 1 HTC Desire HD 1 Samsung Galaxy S
Software | PowerTutor android app for power measurement Audacity for Tone generation Sound Meter android app for ambient noise measurement Audalyzer app as the basis for our application
Notes: Nexus S for measurement. System evaluation we have used other phones.

## Slide 20: Measurement: Indoor Ambient Noise
Indoor (quiet):
42dB (<15KHz), 22dB (>15KHz)
Indoor (canteen):
59dB (<15KHz), 35dB (>15KHz)

## Slide 21: Measurement: Outdoor Ambient Noise
Outdoor (Bus Stop):
61dB (<15KHz), 32dB (>15KHz)
Outdoor (Bus):
63dB (<15KHz), 24dB (>15KHz)

## Slide 22: Measurement: Range Vs Frequency

## Slide 23: Measurement: Multiple Tones

## Slide 24: Prioritization of frequency transmissions
Multiple simultaneous transmission is limited due to noise produced by speaker
Prioritizing newer and locally generated frequencies in the emitter list reduced latency
Frequencies are not accepted into the count unless they appear a fixed number of time

## Slide 25: Conserve Energy By Duty-cycling
Illustration of Counting Process Activity Over Time
Notes: Goertzel detects a specific frequency.

## Slide 26: Impact of Clothing
  People may carry smartphones in pockets
  Clothing could reduce detection range by 50%
  Our Apps can run on wearable devices like Google Glass. This could help overcome impact of clothing

## Slide 27: Outline
Why Crowd Counting?
Why Audio Tones?
Our System
Some Measurements
Evaluation

## Slide 28: Evaluation: Parameters
Parameter | Value
Frequency Range | 15KHz – 20KHz
Guard Band | 50Hz
Tone Width | 400ms
Tones per Transmission | 2
Stabilization time for Count | 5s – 8s
Number of Estimates | 10
Amplitude | 80% Volume

## Slide 29: Evaluation Metrics
Accuracy
Latency of counting process.
Power consumption

## Slide 30: Evaluation: Accuracy In Simulated Scenario With No Ambient Noise
Error is between 12% and 21%. WE USE m = 10
Can count up to 8096 devices

## Slide 31: Evaluation: Scenario For Accuracy Experiment
Indoor
Outdoor (Bus)
Outdoor (Bus Stop)

## Slide 32: Evaluation: Accuracy
Indoor
Outdoor (Bus)
Outdoor (Bus Stop)
Chart: 
| 10 | 20 | 25
Uniform Hashing Approach | 12.8571 | 4.2105 | 26.0444
Geometric Hashing Approach | 35.6352 | 7.3507 | 11.1686
Chart: 
| 10 | 20 | 25
Uniform Hashing Approach | 30.7692 | 29.0196 | 8.339
Geometric Hashing Approach | 24.783 | 13.2011 | 19.6279
Chart: 
| 10 | 20 | 25
Uniform Hashing Approach | 17 | 55.5263 | 24.5333
Geometric Hashing Approach | 14.2837 | 3.1084 | 14.1599

## Slide 33: Evaluation: Accuracy
On average, Geometric hashing accuracy is better than Uniform hashing approach.
In some cases, Geometric hashing error is higher than Uniform hashing. The error remains around the 20% limit which is seen in the simulation.
The only case wherein Geometric hashing error is significantly above 20% limit is because, when the evaluation runs were made for this data point, some of the phones malfunctioned. We retain the result for completeness.

## Slide 34: Evaluation: Count Distribution for (N=25)
Indoor
Outdoor (Bus)
Geometric Hashing: 80% of nodes count between 18 and 27
Uniform Hashing: 80% nodes count between 26 and 36
Geometric Hashing: 80% nodes count between 16 and 31
Uniform Hashing: 30% below 16, 50% between 16 and 31
Deviation in count is higher due to relatively harsher environment

## Slide 35: Evaluation: Single Hop Latency Experiment
Number of Nodes | 2 | 4 | 6 | 8 | 10 | 12 | 15
Latency (in seconds) | 0.43 | 6.1 | 7.4 | 8.0 | 7.8 | 8.1 | 7.5
Single Hop: Scenario
All nodes communicate one-hop
Frequency Division Multiplexing prevents contention
Latency remains constant although nodes increase

## Slide 36: Evaluation: Multi-Hop Latency Experiment
Number of Nodes | 2x2 | 2x3 | 2x4 | 2x5 | 2x6
Number of Hops | 1 | 2 | 3 | 4 | 5
Latency (in seconds) | 6.1 | 11.0 | 17.0 | 19.7 | 20.2
Multiple Hop: Scenario
Increase the number of nodes and number of hops.
Objective is to bring out the multi-hop feature. The effect of hop count on the counting process is also explored.
Notes: Straight line, each chair has 2 phones. Phones are placed such that tones cannot be detected directly by nodes more than one hop away.

## Slide 37: Evaluation: Results for Power Consumption
Settings | Power Consumption (in mW)
3G (ping every 10ms) | 952
WiFi (ping every 10ms) | 480
WiFi (ping every 100ms) | 422
WiFi (ping every 1s) | 65
WiFi (no activity) | 57
BENCHMARK
Notes: Compare with existing technology. One could count using central server and 3g, or AP/WiFi. We try to see how our system fares in terms of energy efficiency compared to these options. We pick the most efficient approach for comparison for baseline which is wifi with no activity.

## Slide 38: Evaluation: Results for Power Consumption
Settings | Power Consumption (in mW)
WiFi (no activity) | 57
Tone counting (FFT, continuously) | 88
Tone counting (FFT, every 350ms) | 73
Tone counting (FFT, every 600ms) | 40
Tone detection (Goertzel, every 1s) | 12
Tone detection (Goertzel, every 5s) | 1.1
Notes: How often we run matters (every 2min)

## Slide 39: Conclusion
We have developed two algorithms to which harness the potential of audio tones to perform crowd counting.
We have built an App that could be installed on any phone with Android operating system and evaluated it in real-life scenarios

## Slide 40: Questions?

## Slide 41: THANK YOU

## Slide 42: References
http://statusmagonline.com/blackberry-and-globe-telecom-present-nicki-minaj/
http://eoc.du.ac.in/images/500px-Speaker_Icon_svgerer.gif
http://roadtointrospection.blogspot.sg/2012/06/10-reasons-your-microphone-is.html
http://www.southerncaliforniarestaurantwriters.net/assets/images/SCRW_banquet2.JPG
http://static.guim.co.uk/sys-images/Money/Pix/pictures/2012/3/16/1331903929152/Tesco-Extra-supermarket-a-007.jpg
http://keropokman.blogspot.sg/2008/05/oh-no-how-to-get-in-bus.html
http://www.flickr.com/photos/seattlemunicipalarchives/2851696370/in/faves-andersonleal/
https://plus.google.com/photos/111626127367496192147/albums/5745849874061604161/5745851316774497090
http://setiathome.ssl.berkeley.edu/plots/timeseries_ap_signal_63515286.jpg
http://689086740.rombla.com/images/bigstockphoto_Audio_Signal_1293091.jpg

## Slide 43: Related Work
Application/Method | Passive Listening | Active Transmission
Environment or Traffic monitoring | NoiseTube, Ear-phone, NeriCell | -
Social context | CenceMe, SurroundSense, Neary | PeopleTones, MoVi
Activity and location tracking/inference | SoundSense, JigSaw, SpeakerSense, Darwin phones, TagSense | -
Data transmission | - | Naratte, Inc., Context-aware computing with sound
Ranging | - | BeepBeep, Centaur(2012)

## Slide 44: Future Work
Low frequency melodies/chirps could be used to penetrate through clothing
Tone width could be used to perform another dimension of encoding
Introduce State/Context based Counting
Could be deployed on wearable devices like Google Glass